## Slide 1: P.E.T.E.R. Progress Meeting
Thomas Keating Ltd.
13/06/2018 – TK, Billingshurst

## Slide 2: Manufacture: TK free-space measurement bench
Free-space materials measurement bench designed and manufactured
To be used for characterising antennas
Sent to University of Stuttgart
New horns not supplied (existing horns to be used)

## Slide 3: Manufacture: corrugated waveguide
Manufacturing of nickel silver corrugated waveguide sections begun
Sections will be soldered together using external tubes

## Slide 4: TK probe parts
Probe with casing
Stainless steel tube
Probe – TK internal parts
Brass cup
Brass or stainless steel probe head
Nickel silver waveguide and probe struts
Probe top
Vacuum valve
Electrical connectors
Microwave window

## Slide 5: PETER probe with VTI
Manufacturing of nickel silver corrugated waveguide sections has begun.
Sections will be soldered together using external tubes.
General assembly drawing for the PETER probe in the VTI (variable temperature insert) with some key dimensions.

## Slide 6: Probe head
Proposed dimensions incorporated into mechanical design
TK Gaussian Beam Mode simulation overlay
Probe head design
Overlap

## Slide 7: TK Gaussian Beam Mode simulation
TK RF design influences:
Mirrors should reflect almost 100 % of beam power (defined by the outer volume shown)
Small beam must be focussed by strongly-curved mirror
Curvature of mirrors cause polarisation distortion

## Slide 8: TK Gaussian Beam Mode simulation overlay
Mechanical design cross-section with microwave beam overlays
Microwave beam overlays with mirrors and mount