## Slide 1: PE EPR microscopy detection methods

## Slide 2: Pros & Cons of the two considered detector methods
Bolometers
Pros | Cons
Extremely wide bandwidth (not limiting factor) Able to use wideband or narrowband source High sensitivity No purchase necessary | Magnitude only Unable to run microscopy and spectroscopy experiments simultaneously
Heterodyne
Pros | Cons
Magnitude & phase Signal enhancement due to technique High sensitivity Able to run microscopy and spectroscopy experiments simultaneously | Bandwidth is limited by multiple factors in current capabilities Limited to narrowband source only Purchase is required (~85-100k€)

## Slide 3: Overall VDI scheme

## Slide 4: VDI source purchase options for narrowband
300 GHz
320 GHz

## Slide 5: Wideband option – roughly corresponds to 5.6 mW
Multiplication factor of 27x and is NOT compatible with heterodyne detection at this time

## Slide 7: VDI: IF and Bandwidth options
High frequency range (GHz) | 290 | 310 | 294 | 306
Low frequency range (GHz) | 12.0833 | 12.9167 | 12.25 | 12.75
Off-set frequency (GHz) | 1 |  | 0.65 | 
Multiplication factor | 24x |  | 24x | 
IF frequency (GHz) | 24 |  | 15.6 | 
Bandwidth (GHz) | 20 |  | 12 | 
Low sideband from mixer (GHz) | 11.0833 | 11.9167 | 11.6 | 12.1
High sideband from mixer (GHz) | 13.0833 | 13.9167 | 12.9 | 13.4
Separation between sidebands (GHz) | 0.1667 |  | 0.15 | 
Separation between sideband and LO (GHz) | 1.6667 |  | 0.8 | 
Cost (k€) | ~92 |  | ~78 | 

## Slide 8: Budget discussion

## Slide 9: Budget: current status of participants
Participant | Funds extrapolated to the end of extension | Use/shift of funds?
BUT | Sufficient funds for extension | 
NGU | Personnel through Dec 2020, 27k€ for consumables, workshops, travel | 
TK | +150k€ (all personnel) | 
USTUTT | + 40 k€ equipment / +6k€ personnel / +10k€ consumables (assumes Martin funded for 8-9 months & Lorenzo though Dec) | 

## Slide 10: Budget: current status of participants
Participant | Funds extrapolated to the end of extension | Use/shift of funds?
BUT | Sufficient funds for extension | 
NGU | Personnel through Dec 2020, 27k€ for consumables, workshops, travel | 
TK | +150k€ (all personnel) | 
USTUTT | + 40 k€ equipment / +6k€ personnel / +10k€ consumables (assumes Martin funded for 8-9 months & Lorenzo through Dec 2020) | 
VDI source
VDI detector
2nd scientific conference
Possible expenditures:
Others…
Lorenzo ??
Extra months for Martin??