## Slide 1: Progresses on Project
UNISTUTT
27 August 2020

## Slide 2
After baseline correction
1st PETER HF-EPR Measurements
We acknowledge Adam Benes for his important contribution

## Slide 3
PETER laboratory
Bolometer
Microwave quasi-optics
Superconducting magnet, 0 - 12 T (Cryogenic Ltd.)
with cryostat enabling EPR measurements from 4 K to RT
PETER sample rod
with SPM unit
SPM unit
SPM probe + probe holder
Sample
Piezoscanner + stepping motors
Microwave waveguide
Coils for magnetic field modulation

## Slide 4
Measurement with Akiyama probe at RT and in Air
Akiyama probe

## Slide 5
Measurement with tuning fork probe with etched glass fiber tip at RT and in Air
Tuning fork probe with etched glass fiber tip
Fabrication:
o
Optical fiber
Optical fiber shield
Hydrofluoric acid (HF)

## Slide 6
Measurement with tuning fork probe with etched glass fiber tip at 77 K in 20 mbar He pressure
Rescaled
Rescaled
At 77 K the scanning range of x,y,z piezoscanners
is reduced by a factor of ~2

## Slide 7
Problems to solve:
Malfunction of the stepping positioner in Z direction – already solved (6. 8. 2020)
Reduction of vibrations transferred to the SPM unit from vacuum scroll pump
through the bellows metal hose – now in process
Input of vacuum scroll pump
(Bellows metal hose)
pump
magnet
Vibration attenuator
(heavy block)
PVC flex vacuum hose
Flexible PVC hose