## Slide 1: Signal localization and BG suppression in THz s-SNOM Rainer Hillenbrand Brno, Oct. 2018

## Slide 2: Standard s-SNOM
P
Ei
Es
Standard s-SNOM with nonmagnetic samples:
External illumination polarizes the tip, yielding the background dipole P0 and creating the hot-spot at the tip apex.
Polarized tip interacts with the sample via near fields in this hot spot yielding, an additional induced dipole Pind
The detected signal is due to radiation of both background and induced dipoles:
Es  P = P0 + Pind
P0 is dominant and is typically suppressed by jittering the tip and demodulating the detector signalat higher harmonic of this jittering frequency.
E

## Slide 3: s-SNOM with magnetic hot spot
s-SNOM with paramagnetics:
We assume that the signal formation mechanism for magnetic antenna tip is similar to that in standard s-SNOM, i.e. the signal is still due to background and induced dipoles (potentially with different polarization):
Es  P = P0 + Pind
Ei
Es
Since the tip is assumed to be nonmagnetic, one can suppress the background scattering associated with P0 by modulating the static magnetic field B0 and demodulating the detector signal at the magnetic field modulation frequency, instead of using the tip jittering technique.
In the following, we analyze the spatial localization (i.e. resolution) of the induced dipole when the tip is not jittered.
Importantly, the analysis presented here is for standard (i.e. electric antenna) tips of nonmagnetic materials. We assume that the signal localization for magnetic antenna tips is similar to that of standard tips with the same tip size and the conclusions of this study will be valid for magnetic antenna tips.
P
B

## Slide 4: Induced vs. Background dipole
Si
h
20 um
Au
R
Pind
10 um
The in-plane resolution directly relates to the vertical localization scale of the s-SNOM signal, i.e.Pind(h) (the height dependence is easier to model than the actual resolution)
Unexpectedly, the vertical localization scale for the induced dipole is 10 um

## Slide 5: Large tips increase near-field signal
tip radius, R [nm]
Field enhancement, E/E0
Tip dipole, P [arb. u.]
Large tips provide larger tip-sample coupling, thus stronger near-field signal, although the field enhancement reduces
R

## Slide 6: Field localization barely depends on tip radius
Surprisingly, the localization scale for the induced dipole is on the same scale 10 um disregarding the tip radius

## Slide 7: High-harmonic Demodulation
s0
s1
s2
normally in s-SNOM the tip is jittered at frequency  nd small amplitude A<< and the signal is demodulated at harmonics n
The demodulated signal can be calculated as
low harmonics contain BG
high harmonics “filter our” the BG and localize signal to the nm scale, but at the expense of signal strength (2 orders of magnitude)
s-SNOM owes nanoscale spatial resolution primarily to the demodulation technique, and not simply small tip radius.
 50 nm
Simulation with A=50 nm

## Slide 8: Signal localization after high-harmonic demodulation for large tips
s2
R=500 nm
R=50 nm
Larger tips provide stronger signal,
yet still offer spatial resolution on the 100 nm scale (for small tapping amplitudes (A<<R)

## Slide 9: Experiment with standard s-SNOM tips
R
Experimental results confirming the signal enhancement by large tips
experiment: signal enhancement
metal
dielectric
experimental resolution
dielectric
metal

## Slide 10: Large tips for boosting magnetic near-field signals the signal
Large tips are suitable for patterning of near-planar magnetic structure that are (potentially) beneficial for EPR detection.
z
x
x
y
z
x
magnetic antenna tip
B

## Slide 12: Conclusions
Without demodulation expect spatial resolution 10 um
Demodulation technique can bring nanoscale spatial resolution down to 100 nm scale, but at the expense of lower signal.
Large tips can boost the signal and provide large area for patterning of magnetic structures.